## Slide 1: Objective
Proliferation of GNSS SDR tech in the past 5-10 years:
GNSS SDR Data Collection Systems
IFEN GmbH
LabSat
Spirent
Loctronix
National Instruments
Averna
TeleOrbit
Nottingham Scientific Ltd.
Many others
GNSS SDR Processing Frameworks
GNSS-SDR
IFEN GmbH
TeleOrbit
Nottingham Scientific Ltd.
GNU Radio
Many university-developed research systems (Colorado, Calgary, Cornell, Ohio, Stanford)
Many government-funded systems
Today: Processors are tailored for specific data format. No established standard to convey GNSS SDR metadata.
Objective: Interoperability between GNSS SDR data collection systems and processors

## Slide 2: Feature Support
In order to support the various types of SDR data file sources and existing and future formats, the standard must support the following data collection topologies and features:
Sample streams that contain multiple bands.
  Adjacent aliased bands that occur in direct RF sampling systems (including spectral inversion of some bands and not others).
  Wideband sampling (e. g. BeiDou B1, GPS L1/Galileo E1, and GLONASS L1 in sampled bandwidth)
Support both IF sampled (real data) and baseband sampled (complex data) streams
Many different sample quantization, numerical representation, and packing formats.
SDR files containing multiple data streams multiplexed in time
  Support for streams of different sample rate and quantization
Files with other data fields in addition to SDR data multiplexed in time
SDR files that are split into multiple files during recording (temporal splitting)
  Each file may contain a single stream or multiple multiplexed streams
  Must support identification of previous and next file of set
Multiple streams saved across multiple files (spatial splitting)
  Must support identification of other files in set
  Support specification of timing offset between data in different files
Combinations of above topologies (spatial-temporal splitting)
General metadata related to data collection (time, location, equipment, etc.)

## Slide 3: Metadata Parameters
To support various topologies, data formats and their combinations, the SDR metadata standard defines a set of parameters to fully describe SDR file(s). We refer to these as metadata parameters. The figure below depicts the hierarchy of metadata parameters.
The following slides define each of these Metadata Parameters
fRF,0
fRF,1
fRF,N
Bands at RF
f
0
SDR Files
Metadata Files
Metadata Parameters
SDR Data Collection System
System
Band
Stream
Lump
Chunk
Lane
File
Event

## Slide 4: Rules
Regardless of data collection topology, each SDR data file shall be paired with exactly one metadata file.
Metadata file extension is that of SDR file extension appended with letter ‘x’. Example: SDR File: ‘FileName.dat’, Metadata File: ‘FileName.datx’
For multiple-streams-in-multiple-files topology, the SDR processor shall know all initial file names.

## Slide 5: System Parameters
Specifies top-level parameters related to data collection campaign and equipment
Parameter | Symbol | Enumeration | Type | Units
Time zone | TIMEZONE | TBD | string (3 letters?) | 
Least common factor sample rate | FSBASE |  | UINT32.UINT32 (N/D) | samples/second
Information relating to data collection campaign | CAMPAIGN |  | string | 
Scenario contained in data | SCENARIO |  | string | 
Information on data collection equipment and/or configuration | EQUIPMENT |  | string | 
Antenna: make, model, type, etc. | ANTENNA |  | string | 
approximate (antenna) location of data collection. Lat, Lon, Height coordinates | LOCATION |  | string | 
Point-of-contact for data collection (person’s name) | POC |  | string | 
Contact info for POC. E.g. email | CONTACT |  | string | 
Table 1. System Parameters

## Slide 6: System Parameters: XML
<!-- System Parameters -->
<TIMEZONE>UTC</TIMEZONE>
<FSBASE>56320000.1</FSBASE>
<CAMPAIGN>Collection Campaign</CAMPAIGN>
<SCENARIO>Specific Scenario</SCENARIO>
<EQUIPMENT>Equipment used: Make/Mode/Serial</EQUIPMENT>
<ANTENNA>Antenna Make/Model</ANTENNA>
<LOCATION>Location Coordinates</LOCATION>
<POC>Entity or person that collected data</POC>
<CONTACT>Contact information</CONTACT>

## Slide 7: Band
fRF,0
fRF,1
fRF,N
Bands at RF
f
fIF,0
fIF,1
fIF,N
Bands at Baseband
f
frequency translation
0
0
A band is defined as a finite span of radio frequency (RF) spectrum.
Band parameters include information on frequency translation to baseband.
Parameter | Symbol | Enumeration | Type | Units
number of bands | NUMBANDS |  | UINT16 | 
containing-stream index | STRIDX |  | UINT8 | zero-referenced index
unique identifier | NAME |  | string | 
RF center frequency | FRF |  | UINT32.UINT32 (N/D) | cycles/second
translated center frequency | FIF |  | UINT32.UINT32 (N/D) | cycles/second
spectral inversion flag | INV | 0: non-inverted 1: inverted | UINT8 | 
approximate double-sided half-power bandwidth | BW3 |  | double | cycles/second
Table 1. Band Parameters

## Slide 8
Band Parameters (XML)
<NUMBANDS>4</NUMBANDS>
<BAND STRIDX="0" NAME=“L1 ANT1” FRF=“1575420000.1” FIF=“13680000.1” INV=“0” BW3=“20000000.1”></BAND>
<BAND STRIDX="1" NAME=“L2 ANT1” FRF=“1227600000.1” FIF=“13680000.1” INV=“0” BW3=“24000000.1”></BAND>
<BAND STRIDX="2" NAME=“G1 ANT1” FRF=“1602000000.1” FIF=“13680000.1” INV=“0” BW3=“26000000.1”></BAND>
<BAND STRIDX="3" NAME=“G2 ANT1” FRF=“1246000000.1” FIF=“13680000.1” INV=“0” BW3=“26000000.1”></BAND>

## Slide 9: Stream
A stream is defined as a series of binary values that are derived from samples produced by a digitizing radio frequency front-end or equivalent source.
Stream sample rate specified as integer multiple (SF) of the system base sample rate fs
Stream data contains information from one or more bands
Front-end samples are conditioned and packed into a stream according to the following stream parameters:
  Baseband or IF sampling (including inversion of numerical values)
  Sample quantization (for baseband sampling, I & Q samples treated as two distinct values with same quantization. i.e. two values for each sample)
  Packed bits per sample (always a power of two)
  Sample encoding scheme
  Packed sample alignment
Stream 0
BPF 0
BPF 1
BPF N
ADC
Band 0
Band 1
Band N
SF0*fs
Front-End 0
sk
sk+1
sk+2
sample
conditioning/
packing

## Slide 10
Parameter | Symbol | Enumeration | Type | Units
number of streams | NUMSTR |  | UINT16 | 
unique identifier | NAME |  | string | 
sample rate factor | SF |  | UINT8 | integer scale factor
sampling method and representation |  | IF, IF’, IQ, IQ’, I’Q, I’Q’, QI, QI’, Q’I, Q’I’ (where ‘ signifies inversion) | string | 
sample quantization | QTZ |  | UINT8 | bits/sample
Packed bits/sample | BTP |  | UINT8 | bits/sample
Sample packing alignment | ALN | ‘L’ – left aligned ‘R’ – right aligned ‘N’ – not applicable | string | 
Sample encoding | ENC | SIGN, SM, INT, BIN, FP | string | 
Stream Parameters

## Slide 11
Sample Encoding Schemes
Bits (QTZ) | Encoding | Set | Range Min | Range Max | Code
1 | sign | {-1, +1} | -1 | +1 | SIGN
2 | sign-magnitude | {-3, -1, +1, +3} | -3 | +3 | SM2
 | signed integer | {-2, -1, 0, 1} | -2 | +1 | INT2
 | offset binary | {-2, -1, 0, 1} | -2 | +1 | BIN2
3 | sign-magnitude | {-7, -5, -3, -1, +1, +3, +5, +7} | -7 | +7 | SM3
 | signed integer | {-4, -3, -2, -1, 0, 1, 2, 3} | -4 | +3 | INT3
 | offset binary | {-4, -3, -2, -1, 0, 1, 2, 3} | -4 | +3 | BIN3
4 | sign-magnitude | {-8, -7,…,-1,+1,…, +8} | -8 | +8 | SM4
 | signed integer | {-8, …, 0…, +7} | -8 | +7 | INT4
 | offset binary | {-8, …, 0…, +7} | -8 | +7 | BIN4
8 | sign-magnitude | {-128, -127,…, +127, +128} | -127 | +128 | SM8
 | signed integer | {-128, …, 0…, 127} | -128 | +127 | INT8
 | offset binary | {-128, …, 0…, 127} | -128 | +127 | BIN8
16 | sign-magnitude | {-215,… ,-1,+1,…, +215} | -215 | +215 | SM16
 | signed integer | {-215, …, 0…, 215-1} | -215 | +215-1 | INT16
 | offset binary | {-215, …, 0…, 215-1} | -215 | +215-1 | BIN16
 | floating point | IEEE 754-2008, FP16 |  |  | FP16
32 | sign-magnitude | {-231,… ,-1,+1,…, +231} | -231 | +231 | SM32
 | signed integer | {-231, …, 0…, 231-1} | -231 | +231-1 | INT32
 | offset binary | {-231, …, 0…, 231-1} | -231 | +231-1 | BIN32
 | floating point | IEEE 754-2008, FP32 |  |  | FP32
64 | sign-magnitude | {-263,… ,-1,+1,…, +263} | -263 | +263 | SM64
 | signed integer | {-263, …, 0…, 263-1} | -263 | +263-1 | INT64
 | offset binary | {-263, …, 0…, 263-1} | -263 | +263-1 | BIN64
 | floating point | IEEE 754-2008, FP64 |  |  | FP64
Other QTZs and encodings exist. WG should determine if we need to specify all of them

## Slide 12
Stream Parameters (contd.)
<!-- Stream Parameters -->
<NUMSTR>4</NUMSTR>
<STREAM NAME=“S0” SF=“1” QTZ=“1” BTP=“1” ALN=“N”></STREAM>
<STREAM NAME=“S1” SF=“1” QTZ=“1” BTP=“1” ALN=“N”></STREAM>
<STREAM NAME=“S2” SF=“1” QTZ=“1” BTP=“1” ALN=“N”></STREAM>
<STREAM NAME=“S3” SF=“1” QTZ=“1” BTP=“1” ALN=“N”></STREAM>
XML:
A sample must always fit within 1, 2, 4, 8, 16, 32 or 64 bits. QTZ, BTP, and ALN specify how extra bits are discarded in the decoding process.
ALN is ‘N’ when QTZ equals BTP (i.e. no extra bits to consider in packed format)
When BTP is greater than QTZ, discard extra bits when decoding (i.e. do not assume sign extension or zero padding)
QTZ, BTP and ALN parameters only specify how quantized samples of a specified encoding are packed. They do not specify which bits are MSB/LSB. This information is specified in chunk parameters.

## Slide 13: Sample Packing Examples
QTZ=3, BTP=4, ALN=L
QTZ=3, BTP=4, ALN=R
valid bits:
discarded bits:
QTZ=4, BTP=4, ALN=N
QTZ=14, BTP=16, ALN=L

## Slide 14: Lump
Samples from multiple coherently-sampled streams may be multiplexed in time to form a single ‘collection’ of sequential samples. This requires parameters to describe how streams are multiplexed. The term ‘chunk’ is used later to describe a segment of data for which an encoding/decoding scheme is specified. Hence, the term ‘lump’ is used to describe the collection of all binary data that gets generated during a single 1/fs sampling epoch.
A lump is defined as the ordered containment of all samples from all multiplexed streams occurring within the interval ts=1/fs
Lumps over time (unformatted)
Stream 0
SF0*fs
Stream 1
SF1*fs
Stream N-1
SFN*fs
SF0 packed samples (real data) or
2*SF0 packed samples (complex data)
Lump

## Slide 15
Parameter | Symbol | Enumeration | Type | Units
number of multiplexed streams | NMXSTR |  | UINT8 | Streams
stream indices (in order of appearance) | STRIDX |  | CSV String of NSTR UINT16 values | Zero-referenced indices
Lump Parameters
<LUMP NMXSTR=“4” STRIDX=“0,1,2,3”></LUMP>
XML:

## Slide 16: Chunk Definition
In general, the sample packing scheme must be known to correctly decode them. For example, consider 16 1-bit real samples packed into a UINT16 word written in little-endian format. These samples would be decoded incorrectly if shifted out from a UINT32 word (due to little-endianness).
Another consideration is whether bits are packed from left to right or vice versa.
A chunk is defined as a segment of data consisting of one or more lumps that has been packed using one of four standard unsigned integer data types.
The Stream, Lump and Chunk parameters together, completely and unambiguously specify the sample decoding scheme.

## Slide 17
Parameter | Symbol | Enumeration | Type | Units
number of lumps | NLMP |  | UINT8 | lumps
packed word type | TYPE | ‘UINT8’, ‘UINT16’, ‘UINT32’, ‘UINT64’ | String | 
number of words | NWORDS |  | UINT8 | words
word endianness | ENDIAN | ‘L’ – little endian ‘B’ – big endian ‘N’ – not applicable | string | 
Padding | PAD | ‘H’ – head padding ‘T’ – tail padding ‘N’ – no padding | string | bits (value implied)
word shift direction | SHIFT | ‘L’ – left shift ‘R’ – right shift | string | 
Chunk Parameters
XML:
<!-- Chunk Parameters -->
<CHUNK NLMP=“1” TYPE=“UINT32” NWORDS=“1” ENDIAN=“L” PAD=“N” SHIFT=“R”></CHUNK>

## Slide 18: Chunk Examples
Examples: Chunk with single lump encoded within single UINT8 word. Lump:
UINT8
NLMP: 1
TYPE: UINT8
WORDS: 1
ENDIAN: N
PAD: T
SHIFT: LEFT
UINT8
UINT8
chunk
t
shift direction
Decoded Streams:
Chunk Parameters:
UINT8
NLMP: 1
TYPE: UINT8
WORDS: 1
ENDIAN: N
PAD: H
SHIFT: LEFT
UINT8
UINT8
chunk
t
shift direction
Decoded Streams:
Chunk Parameters:
UINT8
NLMP: 1
TYPE: UINT8
WORDS: 1
ENDIAN: N
PAD: H
SHIFT: RIGHT
UINT8
UINT8
chunk
t
shift direction
Decoded Streams:
Chunk Parameters:
UINT8
NLMP: 1
TYPE: UINT8
WORDS: 1
ENDIAN: N
PAD: T
SHIFT: RIGHT
UINT8
UINT8
chunk
t
shift direction
Decoded Streams:
Chunk Parameters:

## Slide 19: Chunk Examples (contd.)
Example: Chunk with single lump encoded within single UINT16 word. Lump:
UINT16
NLMP: 1
TYPE: UINT16
WORDS: 1
ENDIAN: L
PAD: T
SHIFT: LEFT
chunk
t
shift direction
Decoded Streams:
Chunk Params:
UINT16
UINT16
b0
b1
b0
b1
b0
b1
UINT16
NLMP: 1
TYPE: UINT16
WORDS: 1
ENDIAN: B
PAD: T
SHIFT: LEFT
chunk
t
shift direction
Decoded Streams:
Chunk Params:
UINT16
UINT16
b0
b1
b0
b1
b0
b1
UINT16
chunk
t
shift direction
Decoded Streams:
UINT16
UINT16
UINT16
UINT16
UINT16
UINT16
UINT16
UINT16
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
NLMP: 10
TYPE: UINT16
Chunk Params:
WORDS: 9
ENDIAN: B
PAD: N
SHIFT: LEFT
Example: Chunk with 10 lumps encoded within 9 UINT16 words. Lump:

## Slide 20: Chunk Examples (contd.)
UINT16
chunk
t
shift direction
Decoded Streams:
UINT16
UINT16
UINT16
UINT16
UINT16
UINT16
UINT16
UINT16
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
b1
b0
NLMP: 10
TYPE: UINT16
Chunk Params:
WORDS: 9
ENDIAN: L
PAD: N
SHIFT: LEFT
Examples: Chunk with 10 lumps encoded within 9 UINT16 words. Lump:

## Slide 21: Frame Definition
A data file may contain other data in addition to SDR data that are multiplexed together. Or, the SDR data may be contained in a payload of a packet (example: when a VITA-59 stream is written to file). At a minimum, the standard must contain information to skip over bytes and point to the start of one or more chunks to be decoded. This is accomplished by defining a frame.
A frame is comprised of a finite integer number of chunks greater than zero.
Chunks within a frame are sequential and contiguous.
A frame may begin with a data segment of arbitrary size (integer number of bytes) known as a header.
A frame may end with a data segment of arbitrary size (integer number of bytes) known as a footer.
A frame may contain data integrity features that are implemented within the header and/or footer segments.
The frame data structure shall be constant for the data collection session (i.e. frame format shall not change dynamically).
chunk
R0
R1
R2
RN
R0
R1
R2
RN
Header
R0
R1
R2
RN
Footer
R0
R1
R2
RN
Footer
Header
Valid Frames:

## Slide 22
Parameter | Symbol | Enumeration | Type | Units
total number of bytes in frame | NUMBYTES |  | UINT32 | bytes
number of bytes in header | HEADERBYTES |  | UINT32 | bytes
number of bytes in footer | FOOTERBYTES |  | UINT32 | bytes
number of chunks in frame | NUMCHUNKS |  | UINT32 | 
Frame Parameters
XML:
<!-- Frame Parameters -->
<FRAME NUMBYTES=“7044” HEADERBYTES=“0” FOOTERBYTES=“4” NUMCHUNKS=“56320”></FRAME>

## Slide 23: Concept of Lanes and Lane Parameters
SDR data collection systems write formatted data into files in numerous ways. We refer to these as system topologies. The main topologies are:
Single ‘stream of data’ written to a single file
Single ‘stream of data’ containing two or more multiplexed streams written to a single file
Two or more ‘streams of data’ written to individual files (each containing one stream, referred to as ‘spatial splitting’)
Two or more ‘streams of data,’ each containing two or more multiplexed streams written to individual files
The term ‘file’ above may be one large file or multiple files split across time intervals (temporal splitting)
The ‘stream of data’ referenced above is typically written to a high-speed disk array. Sector-aligned write modes may be used for performance reasons. For this and other reasons, the start of a frame may not be aligned to the beginning of a file.
For spatially split files, each metadata file must identify its associated SDR file’s association with respect to other SDR files in the data set.
Spatially split files may be written across multiple computer systems. Hence, the time offsets between these systems may be needed to synchronize streams.
The ‘stream of data’ terminology used above is henceforth termed ‘Lane’
A Lane is defined as a conduit that transports formatted data.

## Slide 24
Parameter | Symbol | Enumeration | Type | Units
total number of lanes in data collection system | NUMLANES |  | UINT16 | Lanes
Lane index associated with this metadata file | LANEINDEX |  | UINT32 | zero-referenced index
Time offset of this lane w.r.t. Lane Index 0 | TOFFSETMS |  | UINT32.UINT32 (N/D) | milliseconds
Lane Parameters
XML:
<!-- Lane Parameters --> <NUMLANES>1</NUMLANES>
<LANEINDEX>0</LANEINDEX>
<TOFFSETMS>0.1</TOFFSETMS>

## Slide 25: File Parameters
A file is defined as the ordered collection of bytes retrieved from a single Lane over a finite interval of time that is stored in a digital media device.
Parameter | Symbol | Type | Units
Integer byte offset to start of first frame of Lane | BYTEOFFSET | UINT32 | Bytes
Time that this file was created | CREATIONTIME | TimeCSV string | 
Previous file name of temporally split sequence | PREVIOUSFILE | String | 
Next file name | NEXTFILE | String | 
<!-- File Parameters -->
<BYTEOFFSET>1234</BYTEOFFSET>
<CREATETIME>2014,12,31,23,59,59,999></CREATETIME>
<PREVIOUSFILE></PREVIOUSFILE>
<NEXTFILE>WideBand_1bit_L1L2R1R2_001.dat</NEXTFILE>
XML: